## Slide 1: Wide-Band Spice Model of the High-Speed and High-Voltage Transformers for the CCD220
Jorge Romero
University of Málaga (http://www.uma.es)
Javier Reyes (Presenter), Mark Downing European Southern Observatory, ESO (http://www.eso.org)
Scientific Detector Workshop 2013. 7-11 October 2013. Florence, Italy
Spice Model of the High-Voltage Transformers for the CCD220

## Slide 2
Scientific Detector Workshop 2013. 7-11 October 2013. Florence, Italy
ESO Adaptive Optics Camera
CCD220 is and EMCCD
High-Voltage clock key element for electron multiplication
At the core of the high-voltage clock there is a high-speed transformer
Spice Model of the High-Voltage Transformers for the CCD220
Peak Detector
Peak Detector
High-Voltage PID controller
MOSFET switching at the primary of the transformer
PID controller

## Slide 3
Scientific Detector Workshop 2013. 7-11 October 2013. Florence, Italy
Measurement and Vector Fitting
The S-Parameter measurements have the interesting property that it is not necessary to perform neither shorts nor opens on the network during the measurement process (unlike other kind of representations, say Z or Y parameters)
One can translate S parameter to Z or Y parameters
Spice Model of the High-Voltage Transformers for the CCD220
TWO-PORT
NETWORK
[S]
a1
a2
b1
b2
V1
V2
I1
I2

## Slide 4
10 October 2013
4
Scientific Detector Workshop 2013. 7-11 October 2013. Florence, Italy
Spice Model of the High-Voltage Transformers for the CCD220
Peak Detector
Peak Detector
Very accurate modelling
The extracted model includes:
The effect of the magnetic coupling between the transformer windings
The conductor losses
The interwinding parasitic capacitances
The stray capacitances of the PCB footprint and metal tracks
Model of the transformer
Frequency-response of the resonant circuit.
Fine tuning of the
PID parameters possible
The Spice model
The transformer’s behaviour was accurately modeled as a linear circuit in the Laplace Domain by a network of controlled current and voltage sources.
Time-domain simulation around the resonance frequency

## Slide 5
Scientific Detector Workshop 2013. 7-11 October 2013. Florence, Italy
Unoptimized HV-clock step response
Optimized HV-clock step response
RTD cut on the unoptimized CCD
RTD cut on the optimized CCD
Experimental Results
The oscilloscope shows that the HV-clock of the CC220 varies during the frame readout and variation is proportional to illumination level. This sensitivity to disturbances can be minimized with the proper tuning of the PID controller. Thanks to the accurate model of the transformer the value of the components in the PID have been optimized by simulation to respond quickest to disturbances.
All the simulations have been confirmed by measurements and both agree extremely well. The excellent results speak by themselves.
Spice Model of the High-Voltage Transformers for the CCD220

## Slide 6
Thanks to Jorge Romero and the University of Malaga for this outstanding work