## Slide 1: Focal Plane Array Alignment and Cryogenic Surface Topography Measurements for the Prime Focus Spectrograph (PFS)
Murdock Hart
September 25, 2017
Baltimore, Maryland
1

## Slide 2: Focal Plane Array Alignment and Cryogenic Surface Topography Measurements for the Prime Focus Spectrograph
<number>
Murdock Hart September 25, 2017 SDW2017 Baltimore, Maryland
Micro-Epsilon confocalDT-2451
  White light confocal microscope
  16 micron spot size
  < 0.1 micron error
Wenzel XO-87 Coordinate Measuring Machine
  Precision positioning
  < 0.3 micron error
Vacuum Cryostat
  Measurement performed thru window
  Ambient and cryogenic capabilites
Micro-Epsilon confocalDT-2451
  White light confocal microscope
  < 0.1 micron error
Wenzel XO-87 Coordinate Measuring Machine
  < 0.3 micron error
Vacuum Cryostat
  Measurement performed thru window
  Ambient and cryogenic capabilites
16 CCDs measured average RMS 1.4 micron
8 FPAs assembled average RMS 1.6 micron
  Selective thickness invar shims used for adjustment

## Slide 3: Focal Plane Array Alignment and Cryogenic Surface Topography Measurements for the Prime Focus Spectrograph
<number>
Murdock Hart September 25, 2017 SDW2017 Baltimore, Maryland
Ambient and operating temperature measurements
  CCDs and CMOS devices
Difference topographies shows the effects of thermal cycling on the surface topography
Thermal cycling had a negligible impact upon the surface topogrpahy RMS